## Slide 1: From Storms to Losses: A High-Resolution Model of Windstorm Risk in the Netherlands
m.d.s.fonseca.cerda@vu.nl
11th Workshop on European Storms, June 17th, Delft
Maria Fonseca-Cerda, H. de Moel, J.C.J.H. Aerts, W.J.W. Botzen, T. Haer

## Slide 2
m.d.s.fonseca.cerda@vu.nl
10 out of the 20 most damaging events in the Netherlands are associated with Windstorms
Klimaatschademonitor, VvV (2023)

## Slide 3
If we compare historical records at a proper resolution of both, the characteristics of storms and the damage they have caused, we can get valuable prediction power.
1980
1980
2100
Hazard
Damage
Expected damage
Notes: Understand the Hazard-Loss relationship

## Slide 4: Damage records
Total Damage
Total Insured value
#
Claims
#
Policy holders
Loss ratio
Claim ratio
Postal Code 4-digits (PC4)
=
=
Damage
Notes: Access to insurance data
One of the largest insurance company with coverage throughout the NL

## Slide 5: Hazard data
1980
Reanalysis wind climatology
D – Wind from direction
F – Wind speed
G – Gust wind speed (parametrization)
P – Air pressure
Q – Specific humidity
T – Air temperature
Hazard
2.5 X 2.5 km
Notes: Met. Institution data
From ERA5  Harmonie (numerical model)  downscale reanalysis

## Slide 6
D – Wind from direction
F – Wins speed
G – Gust wind speed
P – Air pressure
Q – Specific humidity
T – Air temperature
Hazard
Damage
Damage
Loss ratio
Claims
Claim ratio
#
Notes: Wind variables correlate well with damage variables
Daily maxima or gust, shouldn’t be used in exchange
Understanding the hazard-loss relation, allows to determine the thresholds where damage starts
  Could guide the decisions for modelling damage
    Very extreme events (low frequency & high intensity) or high frequency & low intensity

## Slide 7
If we compare historical records at a proper resolution of both, the characteristics of storms and the damage they have caused, we can get valuable prediction power.
Wind speed
Gust
Daily maxima
Loss ratio
Claim ratio
Hazard
Damage
#
Spatial analysis
Higher wind speed  more damage in a building & more buildings with damage
#
Notes: Not only loss ratio is important but also the claim ratio
  Not all buildings are damage in a storm
  National level the relationship is log-linear  indication for the resolution of the analysis

## Slide 8
T
Expected damage

## Slide 9
T
Expected damage
€49 million per year
(Excl. 1000-years return period)
Notes: Map shows comb. Intensity of the hazard and exposed assets (& their characteristics)
Higher resolution map
  Identify areas where adaptation should be prioritized

## Slide 10: Hazard evaluation
Extreme Value Analysis
G – Gust wind speed (parametrization)
Extreme Value Analysis
(van den Brink, 2020)
Reanalysis wind climatology
40 years (1979-2019)
Winter months

## Slide 11
Extreme Value Analysis
Annual Maxima
X1/k
Gumbel Fit
Xk
(van den Brink & Können, 2008)
The Netherlands
=1.75
(van den Bosch et al., 2025)
Generalized Extreme Value (GEV)
For ; for :
Where:
Location parameter
Scale parameter
Tail shape parameter
Gumbel (GUM)
For :
Where:
Location parameter
Scale parameter
Tail shape parameter
Notes: Reduce uncertainty related to fitting the parameters
Reduce uncertainty due to the tail shape parameter  specially for higher return periods

## Slide 12
Extreme Value Analysis
Annual Maxima
X1/k
Gumbel Fit
Xk
(van den Brink & Können, 2008)
The Netherlands
=1.75
(van den Bosch et al., 2025)
Notes: Differences in tail (e.g. 1000-years return period)
Gum is more conservative

## Slide 13: Hazard evaluation
Extreme Value Analysis
G – Gust wind speed (parametrization)
(van den Brink, 2020)
Reanalysis wind climatology
40 years (1979-2019)
Winter months
Annual Maxima
X1/k
Gumbel Fit
Xk
Notes: Location & shape parameter per grid cell

## Slide 14: Hazard maps
Extreme Value Analysis
14
Annual Maxima
X1/k
Gumbel Fit
Xk
Notes: Intensity associated with a probability (in this case with a return period)

## Slide 15: Hazard maps
Notes: It is not ‘a storm’, as we are not generating synthetic events
Captures the characteristics of the observe wind speeds during a storm
  Sea – land transition (roughness of the land & urbanization)
  Coast-inland patterns
  Veluwe (wooded area) pattern
Help informing/guiding decision-making

## Slide 16
T
Expected damage
€49 million per year
(Excl. 1000-years return period)

## Slide 17
8,521,658 Residential buildings
(van den Broecke , 2020)
Basisregistratie Adressen en Gebouwen (BAG)
Notes: BAG – eng: Basic Register of Addresses and Buildings
Data of all buildings in NL
Building characteristics  Allow for estimating the Reconstruction Value of the properties
  Year of construction
  Surface area

## Slide 18
T
Expected damage
€49 million per year
(Excl. 1000-years return period)

## Slide 19: Vulnerability
Wind speed
Gust
Daily maxima
Hazard
Damage
Loss ratio
Loss function
#
Probability of loss
#
Claim ratio
(van Ederen et al., 2025)
(Fonseca-Cerda et al., 2024)
Notes: Loss function:
  Asset-level
  RV (building characteristics)
  Estimate of expected loss per property by a given wind gust speed
Claim function:
  Aggregated
  Percentage of damaged properties by a given wind gust speed

## Slide 20: Vulnerability
Loss function
#
Probability of loss
(van Ederen et al., 2025)
(Fonseca-Cerda et al., 2024)
Combined function
Notes: Loss function:
  Potential loss of any building
Claim function:
  Percentage of buildings with damage
Combined function
  Total loss

## Slide 21: Vulnerability
Combined function

## Slide 22
T
Expected damage
€49 million per year
(Excl. 1000-years return period)

## Slide 23
€49 million per year
(Excl. 1000-years return period)
Notes: X-axis (Loss function):
  Potential loss of any building
Y-axis (Combined function)
  Total expected loss
Uncertainty bounds due to the Hazard estimates (per return period)
The larger the T, the larger the Uncertainty (due to the tail behaviour)

## Slide 24: Model validation
Twelve most damaging storms
Modelled risk
Historical damage recorded (VvV)
Comparison
Recorded vs Modelled

## Slide 25: Model validation
Date | VvV1 (€ mln) | Model (€ mln) | Relative error (%) | Relative error (%)
18-01-2007 | 156.17 | 145.45 | -6.86 | -6.86
28-02-2010 | 7.40 | 6.97 | -5.75 | -5.75
28-10-2013 | 92.66 | 51.57 | -44.34 | -44.34
05-12-2013 | 13.92 | 22.06 | 58.48 | 58.48
24-12-2013 | 9.14 | 15.75 | 72.41 | 72.41
31-03-2015 | 32.19 | 18.63 | -42.12 | -42.12
23-02-2017 | 24.80 | 24.84 | 0.18 | 0.18
13-09-2017 | 11.75 | 10.85 | -7.62 | -7.62
03-01-2018 | 34.37 | 27.29 | -20.59 | -20.59
18-01-2018 | 235.34 | 102.08 | -56.62 | -56.62
10-03-2019 | 30.02 | 15.96 | -46.83 | -46.83
09-02-2020 | 46.11 | 58.32 | 26.48 | 26.48
Mean Error (ME) |  |  |  | -16.17
Mean Absolute Error (MAE) |  |  |  | 20.67
1 - Total damage, including business and property insurance claims; 50% of content, and 13% of auto has been removed (VvV, 2023).
Tendency to underestimate total losses (- 16.17%)
Average absolute deviation of 20.67% between the modelled and recorded event losses.

## Slide 26: Limitations
& Opportunities
Uncertainty in hazard estimates propagates into risk estimates, and changes in hazard are not linearly translated into losses.
High-resolution exposure data, but aggregated loss estimates. Further refinement of claim ratio functions could enable higher-resolution and asset-level loss estimation.
Alternative approaches (e.g., machine learning) could be explored to estimate asset-level losses.
Access to more detailed data for calibration and validation would improve model performance and reliability.
The choice of model should be guided by the intended application and decision context.

## Slide 27: A case study of hurricane Kirk (2024)
Collaboration
Hylke de Vries (KNMI)
Maria Fonseca-Cerda (IVM/VU)
Different tracks Plausibly different
Manuscript in preparation
Notes: 9 extreme situation that could already have large impacts (due to CC)
Hurricane Kirk – fast transition from the tropics to the extra-tropics (mid-latitude)
KNMI, data:
  ECMWF ensembles
  Downscaling with HCLIM43 (2.5km resolution)
  Estimate the highest gust  losses

## Slide 28: Climate change Sea Surface Temperature changes (re-simulate with HCLIM43)
Current climate
=> Strong response on changes in SST
(lower pressure, stronger wind gusts, more rain)
SST+2K
Change in SST (degrees)
Potential Losses
in Billions of Euros
Potential losses
€ 2.7 billion
~ 10 Million people experienced
>= Bf12 wind gusts
Manuscript in preparation
Notes: The potential losses estimated using the ‘current climate’ scenario are already very large….
Strong response on changes in SST
Model changes in sea surface temperature to model changes in hazard due to CC
Model losses associated with the hazard changes
Not linear changes

## Slide 29: From Storms to Losses: A High-Resolution Model of Windstorm Risk in the Netherlands
m.d.s.fonseca.cerda@vu.nl
11th Workshop on European Storms, June 17th, Delft
Maria Fonseca-Cerda, H. de Moel, J.C.J.H. Aerts, W.J.W. Botzen, T. Haer

## Slide 30: Different intensities every Kirk-variant differs
=> The lower the pressure, the more wind & rain
Max windgust (m/s)
Max 24h rainsum (mm)
Average over Netherlands
Data: ECMWF ensembles
Min MSLP
(hPa)
Notes: Rain not exceptional (most rain over the sea)

## Slide 31: Strongest wind gusts Downscaling with HCLIM43 (2.5km resolution)
Maximal
Wind gusts
Beaufort
Maximal recorded 52,1 m/s
Minimal MSLP
960,6 hPa
Max windgust (m/s)
Max 24h rainsum (mm)
Average over Netherlands
Data: ECMWF ensembles
Min MSLP
(hPa)

## Slide 32: Costly Impact modelling using VU/IVM. Potential losses to houses and buildings (Fonseca-Cerda et al., 2026)
Potential losses houses & buildings
€ 2.7 billion
Maximal
Wind gusts
Beaufort
Maximal recorded 52,1 m/s
Minimal MSLP
960,6 hPa
~ 10 Million people experienced
>= Bf12 wind gusts
Comparison
Winter storm Eunice (02/2022)
Model € 210 Million
~ €750 million in total
Summer storm Poly (07/2023)
~ €70 million in total

## Slide 33: Model validation
Date | VvV1 (€ mln) | Model (€ mln) | Relative error (%) | Relative error (%)
18-01-2007 | 156.17 | 145.45 | -6.86 | -6.86
28-02-2010 | 7.40 | 6.97 | -5.75 | -5.75
28-10-2013 | 92.66 | 51.57 | -44.34 | -44.34
05-12-2013 | 13.92 | 22.06 | 58.48 | 58.48
24-12-2013 | 9.14 | 15.75 | 72.41 | 72.41
31-03-2015 | 32.19 | 18.63 | -42.12 | -42.12
23-02-2017 | 24.80 | 24.84 | 0.18 | 0.18
13-09-2017 | 11.75 | 10.85 | -7.62 | -7.62
03-01-2018 | 34.37 | 27.29 | -20.59 | -20.59
18-01-2018 | 235.34 | 102.08 | -56.62 | -56.62
10-03-2019 | 30.02 | 15.96 | -46.83 | -46.83
09-02-2020 | 46.11 | 58.32 | 26.48 | 26.48
Mean Error (ME) |  |  |  | -16.17
Mean Absolute Error (MAE) |  |  |  | 20.67
1 - Total damage, including business and property insurance claims; 50% of content, and 13% of auto has been removed (VvV, 2023).
Notes: Potential explanations are that the hazard component is underestimated or that other storm factors (such as duration of the storm) drive losses, which are not captured by our model. On the other hand, it might be that in such events, the content loss of the insurance records corresponds to more than the 50% that is assumed in this study or that businesses present more losses in large and strong events.

## Slide 34: Model validation
Date | VvV1 (€ mln) | Model (€ mln) | Relative error (%) | Relative error (%)
18-01-2007 | 156.17 | 145.45 | -6.86 | -6.86
28-02-2010 | 7.40 | 6.97 | -5.75 | -5.75
28-10-2013 | 92.66 | 51.57 | -44.34 | -44.34
05-12-2013 | 13.92 | 22.06 | 58.48 | 58.48
24-12-2013 | 9.14 | 15.75 | 72.41 | 72.41
31-03-2015 | 32.19 | 18.63 | -42.12 | -42.12
23-02-2017 | 24.80 | 24.84 | 0.18 | 0.18
13-09-2017 | 11.75 | 10.85 | -7.62 | -7.62
03-01-2018 | 34.37 | 27.29 | -20.59 | -20.59
18-01-2018 | 235.34 | 102.08 | -56.62 | -56.62
10-03-2019 | 30.02 | 15.96 | -46.83 | -46.83
09-02-2020 | 46.11 | 58.32 | 26.48 | 26.48
Mean Error (ME) |  |  |  | -16.17
Mean Absolute Error (MAE) |  |  |  | 20.67
1 - Total damage, including business and property insurance claims; 50% of content, and 13% of auto has been removed (VvV, 2023).
Notes: Considering the lower wind gust speeds, it might be that less properties present damages, and our claim ratio function might lead to an overestimation of losses. On the other hand, it might be that in such events, the content loss of the insurance records corresponds to less than the 50% that is assumed in this study

## Slide 35: Hazard maps